## Slide 1: Network Security: GSM and 3G Security
Tuomas Aura

## Slide 2: Outline
Cellular networks
GSM security architecture and protocols
Counters
UMTS AKA and session protocols

## Slide 3: Cellular networks

## Slide 4: History
GSM
  Groupe Spéciale Mobile (GSM) founded in 1982
  Standardized by European Telecommunication Standards Institute (ETSI)
  Renamed Global System for Mobile Communications (GSM)
  First Release in 1990, GPRS (2.5G) in 1997
UMTS
  Universal Mobile Telecommunications System (UMTS)
  Standardized by the 3rd Generation Partnership Project (3GPP) formed by ETSI and Japanese, Korean and Chinese standards bodies
  First Release 1999
  High-Speed Downlink Packet Access (HSDPA) standardized in 2001; came into wide use in 2007-8

## Slide 5: GSM network
Mobile station (MS) = mobile equipment (ME) + subscriber identity module (SIM)
Base station subsystem (BSS) = base station controller (BSC) + base transceiver stations (BTS)
  BTS = base station (BS)
Network switching subsystem (NSS) = mobile switching centers (MSC) and their support functions
  MSC is an advanced telephone exchange
  MSC uses the SS7 signalling network (but moving to IP)
Advanced functions (not covered in this lecture):
  Text messages
  GPRS, HSDPA
  IP multimedia subsystem (IMS)

## Slide 6: GSM network architecture

## Slide 7: UMTS network
Based on the GSM architecture
User equipment (UE) i.e. terminal = mobile equipment (ME) + universal subscriber identity module (USIM)
UMTS terrestrial radio access network (UTRAN) = radio network controller (RNC) + base stations (BS)
Core network = different service domains + home location register
3GPP Release 8 specifies an all-IP network for signalling and data, but deployment will take time
Circuit-switched (CS) domain for voice
Packet-switched (PS) domain for IP data

## Slide 8: UMTS architecture

## Slide 9: Threats against cellular networks
Discussion: What the threats?
Charging fraud, unauthorized use
Charging disputes
Handset cloning (impersonation attack)
  → multiple handsets on one subscription
  → let someone else pay for your calls
Voice interception → casual listening and industrial espionage
Location tracking
Handset theft
Network service disruption
What about intergrity?

## Slide 10: GSM security

## Slide 11: GSM security architecture
Home location register (HLR) keeps track of the mobile’s location
Visitor location register (VLR) keeps track of roaming mobiles at each network
Shared key Ki between SIM and authentication center (HRL/AuC) at the home network
VLR of the visited network obtains authentication triplets from AuC of the mobile’s home network and authenticates the mobile
Encryption between mobile and the base station

## Slide 12: GSM authentication

## Slide 13: GSM authentication
Alice-and-Bob notation:
1. Network → MS: RAND
2. MS → Network: A3 (Ki, RAND)
Ki = shared master key
Kc = A8 (Ki, RAND) — session key
After authentication, BS asks mobile to turn on encryption. A5 cipher with the key Kc

## Slide 14: GSM security
Mobile authenticated → prevents charging fraud
Encryption on the air interface
  → No casual sniffing
  → Encryption of signalling gives some integrity protection
TMSI → not easy to track mobile with a passive radio
Algorithms A3, A8 can be replaced
  AuC and SIM must use the same algorithms
Non-protocol features:
  Subscriber identity module (SIM) card separate from handset
  → Flexibility
  → Thiefs and unlockers don’t even try to break the SIM
  International mobile equipment identity (IMEI) to track stolen devices

## Slide 15: GSM security weaknesses
Only the mobile is authenticated, network not
BS decides when to turn on encryption; mobiles have no indicator
→ Possible to set up a fake BS that uses no encryption
Integrity protection depends on encryption but some networks do not use encryption
Decryption at BS, but BS may be at a hard-to-monitor location and compromised
Early encryption algorithms based on COMP128, which has been broken. A5 cannot be upgraded without replacing the handset
Authentication triplets transferred over the SS7 signalling network, which can be accessed by thousands of operators
No non-repudiation → no protection against false charges from dishonest operators
IMSI sent when requested by BS → IMSI catchers to track mobiles
IMEI not authenticated → can be changed to prevent the tracking of stolen mobiles

## Slide 16: UMTS improvements over GSM
RAN separate from CN
  Roles of radio-network operator and service operator separated
Encryption endpoint moved from BS to RNC
Mutual authentication protocol AKA
Support for multiple service domains
  Circuit-switched, packet-switched, multimedia, WLAN
Protection of core-network signalling
Security indicator to user (e.g. encryption off)

## Slide 17: Counters

## Slide 18: Using counters for freshness
Simple shared-key authentication:
1. A → B: NA
2. B → A: NB, MACK(Tag2, A, B, NA, NB)
3. A → B: MACK(Tag3, A, B, NA, NB)
K = master key shared between A and B
SK = h(K, NA, NB)
Using counters instead of nonce can save one message or roundtrip
1. A → B: —
2. B → A: NB, SQN, MACK(Tag2, A, B, SQN, NB)
3. A → B: SQN, MACK(Tag3, A, B, SQN, NB)
Another benefit: B can pre-compute message 2
A must check that the counter always increases

## Slide 19: Using counters
Counters must be monotonically increasing
  Never accept previously used values
  Persistent state storage needed
Recovering from lost synchronization
  Verifier can maintain a window of acceptable values to recover from message loss or reordering
  Protocol needed for resynchronization if badly off
Values must not be exhausted
  Limit the rate at which values can be consumed
  But support bursts of activity
  Long enough counter to last equipment or key lifetime

## Slide 20: UMTS authentication and key agreement (AKA)

## Slide 21: UMTS AKA
AKA = authentication and key agreement
Based on GSM authentication
Mutual authentication
Sequence number for freshness to mobile → saves one roundtrip to AuC → authentication vectors can be retrieved early, several at a time
  Why is this so important? Why not just use a client nonce?

## Slide 22: UMTS AKA (simplified)

## Slide 23: UMTS AKA (simplified)

## Slide 24: UMTS AKA

## Slide 25: UMTS authentication
Alice-and-Bob notation:
  1. Network → terminal: RAND, SQN⊕AK, f1 (K, RAND, SQN)
  2. Terminal → Network: f2 (K, RAND)
  CK = f3 (K, RAND)
  IK = f4 (K, RAND)
  AK = f5 (K, RAND)
USIM must store the highest received SQN value
AuC must also store SQN and increment it for each authentication
Masking SQN with AK prevents the use of SQN to identify the mobile

## Slide 26
UMTS AKA

## Slide 27
UMTS AKA

## Slide 28: Sequence number SQN
Implementation can be changed in USIM and AuC
  Length is fixed to 48 bits
One suggested implementation:
  SEQ2 — time counter, 224 seconds = 194 days, individual mobile may run ahead of the global time but can never be left behind
  (Note: the clock is local to AuC; mobile has no secure clock!)
  SEQ1 — per-mobile epoch counter, incremented when SEQ2 wraps, or appears to wrap
  IND — partitions the SQN space to independent sequences; highest used SEQ1|SEQ2 stored independently for each IND value 0..31
IND enables creation of multiple simultaneously valid authentication vectors
  Enables buffering of unused authentication vectors in VLR
  Enables parallel authentication in CS, PS, IMS and WLAN domains
IND (5 bits)
SEQ1 (19 bits)
SEQ2 (24 bits)

## Slide 29: Staying in sync
Mobile may run ahead of the global time counter SEQ2 if it needs a burst of values; long-term authentication rate capped at 1/s
Incrementing SEQ at AuC:
  if SEQ2 is less than the global time counter, set equal
  if equal or slightly (at most 216) higher than global time, increment by 1
  otherwise, SEQ2 has wrapped → set SEQ2 equal to global time and increment SEQ1
USIM stores the largest received value of SEQ1|SEQ2 for each IND value 0..31
  If mobile receives a lower or equal value, authentication fails
  If mobile receives a slightly higher value (SEQ1|SEQ2 increased by at most 228 = 8.5 years), USIM updates the stored value
  If the increment is larger than 228, USIM initiates a resynchronization procedure
IND (5 bits)
SEQ1 (19 bits)
SEQ2 (24 bits)

## Slide 30: RSQ Resynchronization

## Slide 31: SQN resynchronization
If USIM receives an SEQ1|SEQ2 value that is too much higher than the previous stored value, it sends AUTS to the AuC:
AUTS = SQN⊕AK, MAC-S
MAC-S = f1*(K, SQN, RAND, AMF) SQN = USIM’s stored sequence number
One extra roundtrip to AuC
  May cause a noticeable delay, similar to when switching on a phone in a new area for the first time
  Only happens in exceptional situations

## Slide 32: Session protocol: encryption
Encryption of MAC SDUs and RLC PDUs between terminal and RNC with the 128-bit session key CK
  BS does not have the key → can use untrusted BS hardware
Ciphertext = PDU ⊕ f8(CK, COUNT-C, bearer, direction, length)
  f8 — based on block cipher KASUMI
  CK = f3(K, RAND)
  bearer – radio bearer identity, to enable simultaneous connection to multiple bearers, e.g. 3G and WLAN
  direction — one bit, uplink or downlink
  length — PDU length
  COUNT-C = HFN|CFN CFN — RLC frame number HFN — hyper frame number, incremented when CFN wraps
  HFN is set to zero when rekeying with AKA

## Slide 33: Session protocol: signalling integrity
Authentication for RRC messages between terminal and RNC — signalling only!
Message authentication code = f9(IK, message, direction, COUNT-I, FRESH)
  f9 — based on block cipher KASUMI
  IK = f4(K, RAND)
  direction — one bit, uplink or downlink
  COUNT-I = HFN|RRC sequence number HFN — incremented if the RRC sequence number wraps
  HFN is set to zero when rekeying with AKA
  FRESH — random nonce chosen by RNC
Monotonously increasing counter COUNT-I protects against replays during one session
USIM stores highest COUNT-I, but RNC might not remember it. FRESH prevents the replay of old signalling messages if the RNC reuses old session keys (need to check the spec for when this can happen…)

## Slide 34: Session protocol: data integrity
Integrity of voice data is not protected
  Bit errors on the radio link are common
  Voice encodings cope well with bit errors
  Resending corrupt data would lead to lower voice quality
Periodic local authentication: counter check
  Terminal and RNC periodically compare the high-order bits of COUNT-C
  Integrity of the counter check is protected by the MAC on RRC signalling
  Release connection if large differences
  Makes it more difficult to spoof significant amounts of data

## Slide 35: UMTS security weaknesses
IMSI may still be sent in clear
IMEI still not authenticated
Non-repudiation for roaming charges is still based on server logs. No public-key signatures

## Slide 36: Backward compatibility
3G users may roam in GSM networks:
  Challenge RAND = c1(RAND)
  Response SRES = c2(RES)
  Encryption key Kc = c3 (CK, IK)
Possible because the keys and algorithms are shared between SIM and AuC only, not by the mobile equipment or radio network

## Slide 37: Exercises
Who could create false location traces in the GSM HLR and how? Is this possible in UMTS?
Consider replacing the counter with a client nonce in AKA. What would you lose?
Try to design a protocol where the IMSI is never sent over the air interface, i.e. the subscriber identity is never sent in clear. Remember that the terminal may have just landed from an intercontinental flight, and the terminal doesn’t know whether it has or not